Technical description:

The ORM 12/24 optical distribution box is designed for the placement of 12/24 optical connectors both indoors and

outdoors. It al ows you use up to two standard smal  cassettes, 12 SC/E 2000, 12x LC duplex, 24x SC/E 2000

connectors.  The  case  is  intended  to  be  wal -mounted  in the  internal space,  or  in the  open  air. The  box  is

equipped with a cylinder lock.

Type:

Grade of coverage:

Inputs:

Colour:

Grade of se guishing:

Dimensions:

Weight:

Accessories:

Accessory bag

Accompanying document

ORM 12/24

IP 54 EN 60529/ IEC 529

2x PG13.5

1x PG29

pale grey RAL 7035

V0 according to the UL 94

320x205x118mm

1.8kg

1pc

1pc

Declaration on product conformance:

The  product  was  manufactured  in compliance  with  valid  technical documentation.  An  observation  of

designed technology procedures and material was followed according to the ISO 9001 standard.

Warranty:

The  manufacturer  guarantees  for  product  imperfections  arised  within period  of  warranty  due  to  the

demonstrably deficient material, error in design, or deficiencies in manufacture. Such a deficiencies shall be

repaired  by  the  manufacturer  free  of  charge. The manufacturer  is authorized  to  reject the complaint  if  the

item  was  demonstrably  damaged  due  to  an  unqualified  infringement,  rough  manipulation,  or  by  force

majeure.  The  warranty  period  is  24  months  (if  not  stated  other  way)  starting  from  the  date  of  product

consignment to the customer. The warranty covers the product capability and conformance with agreed, or

usual purpose.

Note:

The product  design may  vary  as to  used  standard cut-module  girder, lock,  microswitch, e.t.c. according to the

requirement of the customer. The weight of single product execution may vary. MICOS spot s ro. is authorised to

develop its products according to the requirements of the customer. Recording of al  developing changes in this

document is not necessary. Picture is only informative.

Contact:

FONET Kft.

www.fonet.hu

Assembly procedure:

1.  Unlock  the  lock,  slide  the  lid  to  the  right

and remove it.

3.  Using  an  appropriate  tool,  remove  the  outer

jacket from the cable end and clean the gel, if

any, along at least 2 m.

2.  Attach the cabinet at the desired position using

four  wood  screws.  Dril   holes  in  the  wal   for  Ř

8mm plugs.

4.  Remove  the  end  caps  from  the  bushings.  Lead

the optical cables into the cabinet, fix them in the

PG  bushings,  secure  them  in  the  cable  holders

and attach the pul ing components.

drawing

element holder

cable holder,

PVC draw band

5.  Fit  the  holder  with  adapters  and  insert  the

pigtail connectors. Keep the prescribed length

reserves and observe the minimum bending

radius of the optical cables.

7.  Close and lock the inner lid of the distribution

box (by variations).

6. 	Splice  pigtails  to  al   of  the  fibres

(recommended length 1.5 m).  The maximum

length of splice protection is 45 mm. Place the

splices  and  optical  fibre  reserves  into  the

cassette, replace the cassette lid and secure

it with a nut. Introduce the patchcords into the

cabinet  through  the  bushing  and  insert  the

connectors.

8.  Close  and  lock  the  outer  door  of  the

distribution box.

9.  The operations specified in Paragraphs 1-8 may only be performed by an authorized technician.