Type:   	ORM 4

Technical description:

Contact:

FONET Kft.

www.fonet.hu

Optical  distribution  box  ORM  4  is  a  wal -mounted  box  designed  for  the  placement  of  4  optical

connectors  both  indoors  and

Grade of coverage:	IP 54 EN 60529/ IEC 529

Inputs and outputs:	1x PG 9

2x PG 16

Colour:  	pale grey RAL 7035

Grade of self-extinguishing:	V0 according to the UL 94

Dimensions: 	185x103x78mm

Weight:	0,6kg

Accessories:

Accessory bag 	1pc

Accompanying document   	1pc

Optional Accessories:

Post Bracket 	1pc

Base plate with a cover 	1pc

Earthing:

none

Declaration on product conformance:

The  product was  manufactured  in  compliance  with  valid  technical  documentation. An

observation  of designed  technology  procedures  and  material  was  followed  according  to  the

ISO 9001 standard.

Warranty:

The manufacturer guarantees for product imperfections arised within period of warranty due to

the  demonstrably  deficient material, error in  design, or  deficiencies  in  manufacture. Such  a

deficiencies  shal   be  repaired  by  the  manufacturer free  of charge.  The  manufacturer is

authorized to reject the complaint if the item was demonstrably damaged due to an unqualified

infringement, rough manipulation, or by force majeure. The warranty period is 24 months (if not

stated other way) starting from the date of product consignment to the customer. The warranty

covers the product capability and conformance with agreed, or usual purpose.

Note:

The product design may vary as to used optical connectors, lock, according to the requirement of the

customer.

The weight of single product execution may vary. MICOS. spol. s. r. o. is authorised to develop

its products according to the requirements of the customer. Recording of al  developing changes

in this document is not necessary. Picture is only informative.

Assembly procedure:

1.  The  door  shall  be  unlocked,  cover  removed  in

upward direction.

3.  Using  an  appropriate  tool,  remove  the  external

sheathing from the cable end and clean the gel,

if any, along at least 2 m. Remove the end caps

from  the  bushings.  Conduct  the  optical cable

into the box, fix it in the PG bushing and secure

it at the cable holder with a draw band.

5.  Splice pigtails to all of the fibres (recommended

length  1.5  m).  Use  a  microcassette  to  fix  the

splices.  The  maximum	length  of  splice

protection is 45 mm.

2.  The  case  shall  be  mounted  in  the  required

position  by  means  of  two  woodscrews.

Wall  mounting  holes  for  wall  plugs  (dowels)

must be Ř8mm.

4.  For  easier  installation  the  splice  tray  can  be

removed.

6.  Fit  the  adapters  to  the  bearer  and  insert  the

connectors.  Observe  the  prescribed  length

reserves and make sure the minimum bending

radius of the optical fibres is adhered to.

PATCHCORD

PIGTAIL

7.  Cut open the sealing  linings removed from the PG 16 bushings. Insert the patchcords into the cuts

and re-insert the linings into the bushings.

8.  Close  and  lock  the  door  of  the  distribution 	9.  If the cables are placed in raceways, make use

box. 	of the base plate.

10.  If the box is post-mounted, attach the holder to the box from outside using the jointing material. Attach

the box to the post using the stainless steel installation tape “Bandimex”.

11. The operations specified in Paragraphs 1-10 may only be performed by an authorized technician.